Product name : Plastic Turbine Hall water flow sensor meter for water liquid , TDS measurement.
Product item no. : DWS-ML-01
Material : Plastic white
Specification :
Thread size : QUICK link OD6.5mm for ID6MM PE pipe connect
Connect pipe: 6mm
Color :white
Flow rate : 2~30L/ HOUR (Flow pressure must can start up to turn the Turbine running)
Flow Pulse: F(Hz)=(24xQ) L/min +/- 2 %
Max. Working Current : 15mA (DC5 V)
Min. Working Voltage: DC 4.5V
Working Voltage:DC 5V~18V
Load Capacity: =10 mA (DC 5 V)
Pressure :0.1~0.8mPa
Operating Working Temperature :
-25 Degree centigrade to +60 Degree centigrade
Accuracy :+- 2% ，
Wires connection : 3 wires ( red + ; black - , yellow : NPN pulse signal output) ,red blue : TDS measurement

Function : Sensor , flow rate control
Connect pipe: ~ OD9 MM
Color : white
Flow rate : 0.3~10 L/min
Pressure :<0.8mPa
Water pressure resistance : 0.35 Mpa
Voltage range : DC5-24V
Insulation resistance : ＞100MΩ\
Flow pulse characteristics : F=(15*Q-2)±2% Q=L/MIN
Output pulse high level : >DC4.7V (input voltage DC5V)
Max. Working Current : 15mA (DC5 V)
Working Voltage : DC 5V~24V
Load Capacity: =10 mA (DC 5 V)
Operating Working Temperature :
-25 Degree centigrade to +80 Degree centigrade
Accuracy :+- 2%
Cable wire :

red : + : 5V
Yellow : NPN signal output
Black : - GND
Green: NTC temperature sensor 50K.
Blue & Red : TDS ( total dissolved solide) water quality teser sensor.

4 wires :
BLACK -
RED + : comment for temperture NTC
Yellow : pulse signal output ,
Green : NTC temperture,

2 wires :
RED and Blue : TDS Conductivity sens